## Slide 1: Computer Organization and Architecture

## Slide 2: Module Fundamentals of Digital Computer Unit 5 Storage and I/O Interface

## Slide 3: Module: Fundamental of Digital Computer
Unit-5: Storage and I/O Interface
Unit Objectives:
  Objective-1: Illustrate the use of system bus (Knowledge)
  Objective-2: Describe the size of address bus and capacity of memory module (Analysis)
  Objective-3: Explain the need of control bus (Analysis)

## Slide 4: Structure of von Neumann machine

## Slide 5: Computer Components: Top Level View

## Slide 6: Connecting
All the units must be connected
Different type of connection for different type of unit
  Memory
  Input/Output
  CPU (internal to processor)

## Slide 7: What is a Bus?
A communication pathway connecting two or more devices
Usually broadcast
Often grouped
  A number of channels in one bus
  e.g. 32 bit data bus is 32 separate single bit channels

## Slide 8: Data Bus
Carries data
  Remember that there is no difference between “data” and “instruction” at this level
Width is a key determinant of performance
  8, 16, 32, 64 bit

## Slide 9: Address bus
Identify the source or destination of data
e.g. CPU needs to read an instruction (data) from a given location in memory
Bus width determines maximum memory capacity of system
  e.g. 8080 has 16 bit address bus giving 64k address space

## Slide 10: Control Bus
Control and timing information
  Memory read/write signal
  Memory/Input-output
  Interrupt request
  Clock signals
  Synchronization signals

## Slide 11: CPU With Systems Bus

## Slide 12: Memory Connection
Receives and sends data
Receives addresses (of locations)
Receives control signals
  Read
  Write
  Timing (Speed of processor and memory)

## Slide 13: Memory Connection
  Timing (Speed of processor and memory)

## Slide 14: Semiconductor Memory
Type of memory
  RAM
  ROM
Categories of ROM
  ROM
  PROM
  EPROM
  EEPROM

## Slide 15: Input/Output Connection
Similar to memory from computer’s viewpoint
Output
  Receive data from computer
  Send data to peripheral
Input
  Receive data from peripheral
  Send data to computer

## Slide 16: Computer Components: Top Level View

## Slide 17: Data Bus and Address Bus
Size of Address Bus:
SIZE | BINARY | DEC | HEXA | 
8 | 0000 0000 | 0 | 00 | 
8 | 1111 1111 | 255 | FF | 
8 | 0101 0111 | 87 | 57 | 
8 | 0000 0110 | 6 | 06 | 
10 | 11 1111 1111 | 1023 | 3FF | 
12 | 1111 1111 1111 | 4095 | FFF | 
16 | 1111 1111 1111 1111 | 216 -1 | FFFF | 
20 | 1111 1111 1111 1111 1111 | 220 -1 | FFFFF | 
30 | 11 ………………………….. 1111 | 230 -1 | 3FFFFFFF | 
32 | 1111 ………………………… 1111 | 232 -1 | FFFFFFFF | 

## Slide 18: Data Bus and Address Bus
Size of Address Bus and Memory Capacity:
SIZE | BINARY | DEC | HEXA | Capacity
8 | 0000 0000 | 0 | 00 | 
8 | 1111 1111 | 255 | FF | 256
10 | 11 1111 1111 | 1023 | 3FF | 1K
12 | 1111 1111 1111 | 4095 | FFF | 4K
16 | 1111 1111 1111 1111 | 216 -1 | FFFF | 64K
20 | 1111 1111 1111 1111 1111 | 220 -1 | FFFFF | 1M
30 | 11 ………………………….. 1111 | 230 -1 | 3FFFFFFF | 1G
32 | 1111 ………………………… 1111 | 232 -1 | FFFFFFFF | 4G

## Slide 19: Data Bus and Address Bus
Size of Data Bus/Memory Location:
SIZE | BINARY | DEC | HEXA
8 | 0000 0000 1111 1111 | 0 - 255 | 00 - FF
12 | 0000 0000 0000 1111 1111 1111 | 0 - 4095 | 000 - FFF
16 | 0000 0000 0000 0000 1111 1111 1111 1111 | 0 – (216 – 1) | 0000- FFFF
20 | 0000 0000 0000 0000 0000 1111 1111 1111 1111 1111 | 0 – (220 -1) | 00000 - FFFFF
32 | 0000 ………………………….0000 1111 ………………………….1111 | 0 – (232 -1) | 00000000 – FFFFFFFF

## Slide 20: Capacity of memory module
Size of data bus, address bus and memory capacity

## Slide 21: Test Items
Q1. Generally the speed of the memory is slower than the speed of the processor. Why? (Knowledge)
Q2. Explain the characteristics of different kind of ROMs
Q3. A memory module contains 1 G (Giga) memory location, what is the size of the address bus (Analysis)

## Slide 22: Test Items
Q4. Consider a memory module with capacity 4 MB (Mega Byte). What is the size of address bus and data bus if the memory module is (Analysis)
(i) Byte organized
(ii) word organized (word = 16 bits)
(iii) long word organized (long word = 32 bits)
Q5. How to distinguish the address of a memory location and the address of a I/O device if the same address bus is used for addressing. (Design)

## Slide 23: Test Items